## Slide 1: Status of bitumen supplies

## Slide 2
Overview
Presidential task team
Overview of bitumen supply
Overview of bitumen demand
Factors influencing demand/supply
Current supply situation

## Slide 3: Presidential task team
Part of ASGISA is increased investment in infrastructure to meet economic growth goals
Government concerned about key inputs for construction i.e. materials, equipment & skills
Established to study and identify ways to deal with possible bottlenecks
Initiative is to support the achievement of the targets set in ASGISA through the participation of industry

## Slide 4
Bitumen supply
Gaborone
Windhoek
Johannesburg
Mossel Bay
Saldanha
Cape Town
Pretoria
Mbabane
Maputo
East London
Port Elizabeth
Richards
Bay
Durban
Bloemfontein
Kimberly
Maseru
Pofadder
Messina
Pietersburg
Crude oil
refinery
Sapref
Calref
Enref
Natref
Synfuel
plant
Mosgas
Secunda
Sasol
Sasolburg

## Slide 5: Distillation of crude oil
LPG
Petrol
Paraffin
Diesel
Lubricants
Heavy fuel oil
Bitumen
Bitumen is between 1-4% of crude oil consumption
Notes: Because of the differences in carbon numbers and the differences in compound size that it produces, these products have different boiling points. LPG with only 3-4 carbon atom compounds boils between -10 and 15C. Gasoline boils in the range 15 to 150C, lube oil in the range 370 to 525C and so on. Bitumens start to boil in the range 450-550C, a typical value being 525C. It is these differences in the boiling ranges that enables the different products to be separated by a process known as fractional distillation.

## Slide 6: Typical bitumen manufacture
Heavy
crudes
Vacuum
Distillation
Atmospheric
Distillation
Hard
Soft
Bitumen grades
Air
Blowing
Bunker Fuel
Oil
Notes: Blowing air through bitumen makes the bitumen harder, but also changes composition. More about that later in this session. Blowing may be used either to take a soft bitumen and make it harder, because you haven’t got the distillation ability to cut deep enough to make it to the desired grade. Or you can take a bitumen which would be slightly out of spec, and bring it in spec. Also used to make PPA into bitumen.

## Slide 7: Overview of bitumen supply
4 crude oil refineries that manufacture bitumen
Between 1 – 4% of crude oil is used for bitumen
Portion of residue not used for bitumen is processed into BFO (i.e. 15 – 25%)
Bitumen production has exceeded local demand
60% of capacity situated at Durban resulting in exports mainly to Indian Ocean Islands

## Slide 8: Supply of bitumen in 2006

## Slide 9: Bitumen refining capacity
Potential capacity = +-725k ton
Spare capacity = +-253k ton if:
  Refineries increase storage and loading capacity
  Natref continue to produce at same rate
  No increase in export volumes
561k ton available for local market

## Slide 10: Bitumen refining capacity

## Slide 11: Overview of local demand
Volume has declined from 400k tons in late ’80s
Fluctuated around 250k tons (+-%5) over past 5 years
Experienced dramatic growth of 17.5 % in 2006 to 308k tons
If growth continues at 17% then capacity will be reached by end 2010 i.e. 561k ton

## Slide 12: Factors affecting local demand
Short term fluctuations
Seasonal climatic conditions
  Use of emulsions
Financial year end
  Increase budget period
Annual construction shutdown
  Reduce the length of S/D period
  Rather S/D in winter

## Slide 13: Bitumen consumption in 2006
1
2
3
3
3

## Slide 14: Factors affecting supply
Short term
Scheduling of refinery shutdowns
  Unavoidable to spread to accommodate international expertise required
Limited storage and loading capacity
  Increase dispatching capacity to improve turnaround time of road tankers
Loading bulk bitumen into ships
  Erection of bulk tankage at wharfage to reduce peak demand

## Slide 15: Longer term issues
Future position of Natref towards refining bitumen
Exporting of bitumen
Importing of bitumen
Sufficient refining capacity to meet future demand by:
  Processing increasing percentages of residual crude oil
  Increased investment in blending and dispatching facilities

## Slide 16: Current supply situation
Sapref
  Unable to produce since SD at end of last year due to a fire
Natref
  Forced to reduce production levels by half due to lightening strike in Dec on one of the crude tanks
  Damaged tank repaired and back to normal
Caltex
  SD for 6 weeks from 19 March
  Managed to supply bitumen during SD
Volumes up for first quarter by 25%

## Slide 17: Short term availability
Sapref & Caltex
  Expect to return to full production shortly
Natref
  SD planned from 8 May to 16 June
  Limited stocks available until end May
  Bitumen only available early July
Engen
  SD planned from 4 June to 6 July
  Limited stocks will be available

## Slide 18: Summary
Sufficient inherent refinery capacity to meet demand
Refineries need to:
  Upgrade dispatching capacity to improve turnaround time of road tankers during peak demand
  Increase blending capacity to cope with increased long term demand
Prime marketers need to:
  More flexible wrt export orders
Secondary producers need to:
  increase their own bitumen storage capacity to cope with peak demand
Road authorities need to:
  Spread periodic road maintenance over the year to reduce peak demand on resources