## Slide 1: SANRAL Overload Damage Quantification Louw Kannemeyer

## Slide 2: Pavement Damage
Non-Traffic Associated Damage
  Rainfall (Moisture) – Materials Strength Reduced
  Ultra Violet Radiation – Ageing of Surface Materials
Traffic Associated Damage
  Axle Loads - Overloading
  Tire Pressure – New Tire Technology

## Slide 3: TRAFFIC ASSOCIATED DAMAGE Axle Loads - Control
Axle Loads
  Legal Limits
  Effective Enforcement
    Network of Traffic Control Centers
    Operated 24 hours 365 days a year
    Zero Tolerance to offenders
    RTMC
Mantsole TCC – N1 North of Pretoria
9,0 Tons
7,7 Tons

## Slide 4: TRAFFIC ASSOCIATED DAMAGE Tire Pressure
Tire Pressure
  Not Practical to Specify Legal Limits
    Technology Improvements Driven by Quest for Economic Efficiency
  Improved Design Procedures & Materials Through Research
    Accelerated Pavement Testing (APT)
    Stress-In-Motion (SIM)
Stress In Motion
HVS VI+

## Slide 5: Toll Concessions - Background
The risk associated with the damage caused by overloaded axles remain with the Implementing Authority – SANRAL
Additional damage caused by overloaded axles impacts the concessionaire as follow:
  Time-shift Costs: planned maintenance and rehabilitation actions have to be performed earlier than originally planned due to the higher number of axles applied, this results in the concessionaire having to secure funding earlier, which results in interest payments over longer period than originally planned,
  Additional Strengthening Costs: the additional axles due to overloading consume pavement structural life, resulting in additional strengthening required to ensure pavement lasts for the concession period.

## Slide 6: Overload Damage - Cost Recovery
Load P
Legal portion
Overloaded
portion
Actual field condition
Damage
Determined by P and pavement sensitivity
Cost
Cost recovery
Compensation
Toll

## Slide 7: Methodology
The approach is based on comparing the without overloading to the with overloading scenario, taking into consideration the load sensitivity of the specific road pavement structures on these road sections – based on published results
  - field observations will introduced complex construction related variables,
Based on collaboration between various parties involved:
  Concessionaires with his Technical Specialists
  CSIR
  Africon
  Prof Christo van As
  SANRAL

## Slide 8: Equivalent Damage Calculation: With Overloading
Axle load interval
Axle counts
Legal axle load
n1
n2
ni
nk
nl
Axle load interval
LEF
Legal axle load
LEF1
LEF2
LEFi
LEFk
Axle load histogram
Load equivalency
x
LEFl
AASHTO METHOD: Published values of load sensitivity for generic road pavement types according the AASHTO procedure used internationally,
SOUTH AFRICAN MECHANISTIC DESIGN METHOD (SAMDM): Mechanistic-empirical modelling using the South African Mechanistic Design Method

## Slide 9: Equivalent Damage Calculation: Without Overloading
Axle load interval
Axle counts
Legal axle load
n1
n2
ni
nk
nl
Axle load interval
LEF
Legal axle load
LEF1
LEF2
LEFi
Axle load histogram
Load equivalency
x
LEFl
Axle Load Histogram: Based on the actual measured traffic axle load data obtained to date using Weigh–-In-Motion (WIM) technology.

## Slide 10: Time Shift Costs
No Overloading
With Overloading

## Slide 11: Additional Strengthening Cost