## Slide 1: Revision of the South African Pavement Design Method Louw Kannemeyer

## Slide 2: Aka GODZILLA

## Slide 3: Historical overview – SAMDM development
Origin of Current SAMDM – Damage Models
    Fatigue of asphalt concrete wearing courses
      Freeme – 1970s
    Fatigue of asphalt concrete base layers including temperature
      Published data – 1970s to 1980s
    FoS permanent deformation for unbound material
      Maree – 1970s to 1980s
    Effective fatigue and crushing failure for cement stabilized layers
      de Beer – 1980s
    Vertical strain criteria for subgrade
      Dorman and Metcalf – 1965
New Tire Technology
Increased Tire Pressure

## Slide 4: SAMDM - Current status
Past implementation exposed all the weaknesses of the method
Users became disillusioned with the method
  Counter-intuitive and inadmissible results
  Extreme sensitivity of the method to input
  Inconsistent input
    Resilient response (FWD, MDD, Laboratory)
    Strength parameters
Statements made that ME-design is not possible
  Too many unexplained effects (chaos)
  Design can only be based on past performance (LTPP, rehabilitation investigation, etc.)

## Slide 5: R&D Dream #1: Close Gap Between Reality and Theory
Adjust the Theory to Predict Reality
Theory
Reality
Rut
Terminal rut
Roughness
Terminal IRI
Extent of fatigue
Time

## Slide 6: R&D Dream #2: Levelling the Playing Field
Overall system just as good as Weakest Link

## Slide 7: R&D Dream #3: Single “Tool” – Different User/Risk Levels
Young professional
Seasoned professional
Design
Specialist
Design scenario:
Routine and preliminary design
Low risk
Low design experience
Known materials – default input
Conventional material classification
Design scenario:
Important design
Medium risk
Seasoned professional designer
Project specific input
Design scenario:
Very important design, high risk
Special investigations
Specialist designer
Unusual materials
Project specific input
User
Design application

## Slide 8: Research and Development (R&D) Framework
Pavement Design Task Group
  Established May 2005
  Series of meetings during July and August 2005
  R&D framework submitted in November 2005
    Characteristics of new pavement design method
    R&D topics
      Demand analysis (Traffic and environment)
      Material resilient response models
      Pavement resilient response models
      Damage models
      Probabilistic and recursive schemes
    Each R&D topic have a number of identified R&D needs
    Each R&D need translated into one or more project briefs to address the need – November 2006

## Slide 9: Project Objectives
Overall objective
  To develop a design method that is
    Accurate (agree with reality)
    Impartial in terms of pavement type selection
      Unbound (Crushed stone, natural gravel)
      Stabilised (Cement, Foamed-bitumen, Emulsified-bitumen)
      HMA
      Concrete (not included in flexible pavement design R&D process)
Project structured according to immediate, short, medium and long-term objectives and deliverables
  Achievement of immediate, short, medium and long-term objectives subject to availability of resources

## Slide 10: Time-frame for R&D process
Immediate | 12 to 18 months
Short-term | 3 to 5 years (1.5 to 3 years)
Medium-term | 5 to 8 years (3 to 5 years)
Long-term | 8 to 12 years >5 Years

## Slide 11: R&D Process
Project funding and contracts
  Funding organisations will sponsor projects of interest to them
  Contract between service provider and project client
Project management
  Phase 1 – Develop Detailed Project Briefs - Done
  Phase 2 - Inception Phase (In Progress – 27th June 2007)
    Investigate available solutions
    Finalize project methodology
    Finalize cost and resource allocation
  Phase 3 – Delivery of immediate, short, medium deliverables (Anticipated Start Date – November 2007)

## Slide 12: R&D Process (continued)
Overarching integration level project
  Integration of output from various ME-design related projects
  Integration of performance based information system with ME-design components in a single design method
Delivery mechanisms
  Website for tracking progress on R&D process and sharing general information
    Any content (documents and software) developed as part of the project available for use on the project website
  Immediate, short, medium and long-term output
    User-manual with an overview of the method
    Detail technical documents on individual components
    Technical guidelines, test protocols and method specifications

## Slide 14
Temperature
Moisture
content
Density
Grading
Atterberg
limits
Binder
content
Binder
properties
Geometry
PB/2006/A-2
Other?
Other?
PB/2006/A-1
Grading
PB/2006/B-1b
PB/2006/B-1a
PB/2006/B-1c
UCS
Stress and
strain at break
Time/previous
loading
HMA
Unbound
Stabilized
PB/2006/B-4
PB/2006/A-3
PB/2006/A-4
PB/2006/C-1
PB/2006/C-3
PB/2006/C-4
PB/2006/C-5
Resilient
response models
Damage models
PB/2006/D-1
HMA
Unbound
PB/2006/D-2
Other?
Stabilized
PB/2006/D-3
Subgrade
PB/2006/D-2
PB/2006/E-3
Computer
solution
PB/2006/E-1 and PB/2006/E-2
PB/2006/B-2 and PB/2006/B-3
PB/2006/C-2
PB/2006/B-4

## Slide 15
Immediate
Short-term
Medium-term
PB/2006/A-1
Tyre loading and contact stress information system
Information system shell with available data
PB/2006/A-4
Effects of vehicle dynamics on traffic input for pavement design
Forward modelling of dynamic axle load spectra
Backward modelling of static axle load spectra
PB/2006/A-3
Traffic survey and design traffic calculation guidelines
A contact stress and traffic survey strategy for southern Africa
Dynamic error adjustment
Revision of guidelines and method specifications`
Ongoing population of information system
PB/2006/A-2
Traffic volume and axle load information system
Information system shell with available data:
Data filters
Bias adjustment
Random (dynamic effect) error adjustment
Ongoing population of information system
PB/2006/C-1
PB/2006/ILP
Integration level project
Guidelines and method specs for contact stress and traffic surveys
TMH 8 & TRH 16
Training material

## Slide 16
Immediate
Short-term
Medium-term
PB/2006/C-3
PB/2006/B-4
Calibrated models for an extended range of materials
A design input information system for road-building materials
Updated refusal density models
Calibrated resilient response models
PB/2006/B-3
Guidelines
Material testing, interpretation of results and deriving design input
PB/2006/B-1a
Resilient response models for unbound material
Static model = f (D, MC, σ)
Dynamic model = f (D, MC, σ)
Test protocols and model calibration procedures
Ongoing model calibration
Link to engineering parameters
Long-term changes
PB/2006/B-1b
Resilient response models for HMA material
Static model = f (T, mix)
Dynamic model = f (T, mix)
Test protocols and model calibration procedures
Ongoing model calibration
Long-term changes
Link to engineering parameters
Resilient response master curves
PB/2006/B-1c
Resilient response models for stabilised material
Tri-axial or flexural testing?
Static model = f (mix)
Dynamic model = f (mix)
Test protocols and model calibration procedures
Ongoing model calibration
Long-term changes
Link to engineering parameters
PB/2006/B-2
Agreement between resilient modulus results from different tests
Guidelines for deflection bowl utilisation
Fundamental principles of different tests
Static and dynamic back-calculation
Agreement between test methods
PB/2006/ILP
Integration level project

## Slide 17
Immediate
Short-term
Medium-term
PB/2006/C-1
Improved modelling of non-uniform contact stress distribution
Closed form solution for circular, non-uniform 3D contact stress
Finite element (FE) solution for irregular shape, non-uniform 3D contact stress
PB/2006/C-2
A benchmark of stress and strain in a variety of pavements
1st order system for measuring T, σ, , , psuc
Benchmark set of T,σ, , , psuc
Wireless intelligent aggregate
Additional T, σ, , , psuc
PB/2006/C-3
Modelling vertical and horizontal variation in pavement response related to the temperature and stress dependency of materials
Closed form solution
Temp. gradient in AC
Dens. and MC gradient in unbound
Effective stress in unbound
Stress dependency in unbound
FE solution
3D variation in temp. dens. MC and stress condition
Thermally coupled analysis
Effective stress in unbound
PB/2006/C-4
Improved modelling of geometric non-linearity
Closed form solution with layer slip
FE solution with cracks
FE solution
Perfect plasticity
Dynamic response analysis
Closed form visco-elastic solution
PB/2006/C-5
Improved modelling of material non-linearity and dynamic pavement response
FE solution
Visco-elasto-plastic
PB/2006/ILP
Integration level project

## Slide 18
Immediate
Short-term
Medium-term
PB/2006/D-3
Improved damage models for stabilized material
Final recommendation on appropriate damage models;
Accelerated curing procedures for simulating short and long-term aging;
Test protocols for yield strength, plastic strain and flexibility testing;
The effect of long-term changes on the yield strength, flexibility and plastic deformation resistance;
Recalibration of the effective fatigue damage model for cement-treated material.
Yield strength, plastic strain and flexibility models calibrated for a comprehensive range of stabilized materials at different stabilizer contents and different stages of curing
PB/2006/D-1
Improved damage models for bituminous materials
Fatigue damage models based on overseas research
Plastic strain predictive models
Test protocols and damage model calibration procedures for bituminous material
PMS based damage distributions and expected life for surface seals and non-structural thin layer bituminous surfacings
SA based fatigue and plastic strain damage models for HMA surfacing and base courses
Mechanistic damage models for seals and non-structural thin layer bituminous surfacings
PB/2006/D-2
Improved plastic strain and shear damage models for unbound material
A subgrade permanent deformation damage model
Calibrated yield strength and plastic strain damage models for unbound structural layers
Test protocols and model calibration procedures for unbound material
Ongoing calibration of yield strength and plastic strain damage models
Continuous damage models for non-linear recursive analysis
Yield strength and damage models related to engineering parameters
PB/2006/B-3
PB/2006/B-4
PB/2006/ILP
Integration level project

## Slide 19
Immediate
Short-term
Medium-term
PB/2006/E-2
Guidelines on the collection and interpretation of statistical data
Guidelines for collecting sufficiently large data samples and method specifications for statistical analysis and interpretation of the input data for new and rehabilitation design;
Training material on the content of the above documents.
PB/2006/ILP
Integration level project
PB/2006/E-1
Actual spatial and time variation of field variables, engineering parameters and the environment
Information system shell for
Spatial and time variation of field variables and engineering parameters
Spatial and time variation of environmental variables
Ongoing population of information systems
Models relating pavement conditions to environmental variables
PB/2006/E-3
Design risk analysis and pavement performance simulation
Probabilistic simulation on design traffic and bearing capacity estimation to calculate design risk.
Linear recursive simulation for time-based modeling of pavement performance
Non-linear recursive simulation for time-based modeling of pavement performance