## Slide 1: Binder Distributor Certification
21 November 2007
RPF Pretoria

## Slide 2: History of events
RPF task team formed in May 2002 to address issues related to the use of Binder Distributors
Resolution passed at RFP in May 2003 to develop a frame work for accrediting BD
BD accreditation scheme proposed by Barry Dumas of PAWC and accepted @ RPF in November 2003
Sabita appointed VKE in November 2004 to draft a manual on the requirements and testing of BD to replace outdated TMH 2

## Slide 3: Implementation of BD accreditation scheme
Based on the Australian scheme
Industry should strive to be self regulatory
Appoint an independent service provider to conduct calibration of BD at client fixed pit facilities
Service provider to comply with ISO/SANAS requirements
National service provider to issue calibration certificates for each binder distributor
Sabita to post details on each binder distributor on their website

## Slide 4: Binder Distributor issues
Poor correlation between fix pit transverse calibration and ‘bakkie’ test
  Testing oil does not emulate high viscosity modified binder properties
Does not accommodate new generation sprayers
  Forward speed is integrated with pump output to ensure correct application rates
Current BD calibration system does not guarantee field performance
No standard procedures for conducting BD calibration test
  test methods to be compliant with acceptable standards

## Slide 6: Latest developments
Sabita to submitted a proposal to KZN DoT and GPTRW to outsource certification testing at their fixed pit facilities
Drafting of BD test methods into SANS format for on-site and at operators premises

## Slide 7: SANS test methods for BD
Property
Verification of dipstick
Power & road speed indicator test
Pump system performance
Tranverse distribution of a BD (Bakkie test)
SANS method
3001-BT20
3001-BT21
3001-BT22
3001-BT24

## Slide 8: Proposed system
Goal
  Implement depot & on site testing to ensure ‘fit purpose’ with project binder
Propose procedure
  Conduct all tests at operator premises prior to start of project
  ‘Bakkie’ test to be done on site as a control during project
Record of all tests to be kept in BD orange box

## Slide 9: Contractual issues for testing
Need to agree conditions when retesting is required
  Initial testing for contractors account
  Additional testing for client’s account
  If additional test results fail then for contractors account
Contract documents to reflect above
  Must include pay item for addition tests

## Slide 10: New approach
The initial calibration of BD to become the responsibility of equipment manufacturer
General requirements for road worthy will remain responsibility of BD owner
Sabita to publish a guideline on mechanical performance requirements and testing of BD

## Slide 11: New approach
Simple assessment of BD so that it can be done anywhere ie not limited to 2 fixed pit testing centres
What should be checked:-
  Mechanical condition (BT21 and by
  observation BT22)
  Pump system output (BT22, also cover
  dipstick and thermometer checks)
  Transverse distribution (BT24)

## Slide 12: New approach
What equipment / facilities would be required over and above normal BD operational needs?
  Trough of capacity at least 2 500 L
  Buckets for BT24
  For more permanent facilities a sophisticated volume measuring system :-
    Flow-meter
    Weighing system

## Slide 13: New approach
Three situations envisaged:-
  Large projects – tests carried out on site
  Small / occasional work – tests carried out in
  BD owner’s yard shortly before use
  3. General competency (for those who don’t know or care) – tests carried out in BD owner’s yard on a regular basis (annually?)
  Tester:-
  Testing for 2 and 3 supervised by independent accredited tester

## Slide 14: New approach
Testing fluid:-
  General – emulsion
  Specific – project binder
This approach has been discussed with industry stakeholders at a meeting held 19 November who have reacted favourably
Mindset change – think of checking rather than calibration or certification.
New approach allows to check if BD is ‘fit for purpose’

## Slide 15
From tray
Bucket
to