## Slide 1: Technical Recommendations for Highways No 12 TRH 12
<footer>
<date/time>

## Slide 2: Technical Recommendations for Highways No 12 TRH 12
1980
1983 – draft TRH 12: Bituminous pavement rehabilitation design
1983 1989 1990
1990 – draft TRH12: Flexible pavement rehabilitation investigation and design - 1997

## Slide 3: 1983 draft TRH 12: bituminous pavement rehabilitation design
Initial assessment
Detailed assessment
Rehabilitation design
Economic analysis

## Slide 4: 1990 &1997 draft TRH 12: flexible pavement rehabilitation investigation and design
Managerial inputs
Condition assessment
  Initial assessment (evaluation criteria)
  Detailed assessment
Rehabilitation design – applicability - refer to detailed documents
Practical and functional aspects
Economic analysis

## Slide 5: draft TRH 12: flexible pavement rehabilitation investigation and design
Latest revision:
2004 – Need identified – RMC of COTO
22 July 2004 – Symposium in Cape town
- feedback from industry/role players
15 Nov 2004 – Workshop at Gautrans
27 Jan 2005 – Needs list of all inputs received

## Slide 6: draft TRH 12: flexible pavement rehabilitation investigation and design
SANRAL funding
SANRAL coordinate for RMC
Chair – Mr JC van der Walt (SANRAL)
  Manager - Mr R Lorio (SANRAL)
  Members – Industry/Universities/private practice
First meeting – 14 July 2005
  Confirm scope

## Slide 7: draft TRH 12: flexible pavement rehabilitation investigation and design
Scope:
Include new/improved knowledge
Definitions & back ground information
Change tone – step by step & check lists
Provide guidelines :
  type & accuracy of information needed
  Details on the use of information
Examples & photographs
Layout of document

## Slide 8: draft TRH 12: revision
Very comprehensive revision
First draft – 31 May 2006
Committee Meeting - 3 August 2006
  Work groups
Detailed workshop 12 &13 Oct 2006

## Slide 9: draft TRH 12: Flexible pavement investigation, analysis and rehabilitation design
<footer>
<date/time>
Introduction
Non pavement related aspects influencing pavement rehabilitation design
Pavement Condition Assessment
  Initial assessment
  Detailed assessment
Rehabilitation options and design approach
Life cycle cost comparisons

## Slide 11: 2006 – draft TRH12
<footer>
<date/time>
1 Introduction
1.1 Background
1.2 Scope
1.3 Pavement “life”
1.4 The art of pavement rehabilitation design
1.5 Managing pavement rehabilitation design
1.6 Recommended approach

## Slide 12: Pavement “end of life”
End of “optimal functionality”
  Service will continue - BUT
    Risk to road user
      Safety considerations
      Road user costs
    Risk to road authority/owner
      Costs (maintenance & rehab)

## Slide 13: The “art” of pavement rehabilitation design
Perception: relatively simple
  Low risk of disastrous consequences
  Professional risk
  Lack of accountability
  however

## Slide 14: The “art” of pavement rehabilitation design
Fact : complex structures
Pavement engineer – optimal (cost effective) design:
  Materials (various types, large variability)
  Construction techniques
  Moisture control & drainage
  Evaluation tests/methods
  Design methods (applicability)
  Environmental conditions & influence
  Life cycle cost comparison techniques
  etc
“ forensic investigation”

## Slide 15
Optimal design
Conservative design
Increase in risk
Acceptable risk
Increase in expertise
Increase in rehabilitation construction costs
High risk
Low risk

## Slide 16
MANAGEMENT
CONSIDERATIONS
SECTION 2.1
Commission project level rehabilitation investigation and design projects
SOCIAL/ENVIRONMENTAL
CONSIDERATIONS
SECTION 2.2
PRACTICAL & FUNCTIONAL
CONSIDERATIONS
SECTION 2.3
CONDITION
ASSESSMENT
SECTION 3
REHABILITATION DESIGN
SECTION 4
LIFE CYCLE COST
COMPARISON
SECTION 5
NETWORK LEVEL INVESTIGATIONS:
ROAD MANAGEMENT SYSTEMS
PROJECT LEVEL INVESTIGATIONS
TRH12

## Slide 18: Section 2: Non pavement related aspects influencing rehabilitation design
2.1 Introduction
2.2 Management considerations
2.3 Social and environmental considerations
labour int; OH&S; EIA
2.4 Practical & function aspects
2.5 Checklist

## Slide 29: Pavement surveillance
Input data sensitive
  type of measurement
  frequency - accuracy

## Slide 31: Traffic loading
Guidelines
  Detailed load surveys
  Estimates – traffic volumes
Updated E80 values
E80 growth rates
Example – sensitivity analysis

## Slide 32
TABLE 3.963: E80 factors for different
heavy vehicle groupings
HEAVY VEHICLE GROUPING | TRH 16 (1991) |  |  | SATCC (1998) |  |  | CTO STATIONS (1986-2002) HSWIM# |  | 
 | Low | Med | High | Low | Med | High | Low | Med | High
2 + 3 Axles | 0.6 | 1.2 | 1.9 | 0.4 | 1.8 | 2.5 | 0.7 | 2.0 | 2.5
>3 Axles | 1.6 | 3.0 | 4.1 | 1.2 | 4.1 | 5.5 | 1.9 | 3.7. | 5.0
Short (2 axles) | 0.3 | 0.7 | 1.1 | 0.3 | 1.5 | 2.0 | 0.3 | 0.9 | 1.7
Medium (3+4 axles) | 0.8 | 1.8 | 2.8 | 0.6 | 2.3 | 3.3 | 1.0 | 2.1 | 3.1
Long (>4 axles) | 2.1 | 3.4 | 4.4 | 1.4 | 4.6 | 6.2 | 2.2 | 4.2 | 5.6
Low

## Slide 33: Processing of data
Facilitate objectives of the initial assessment
  Identify uniform pavement sections
    Differences in;
      Visual condition (S – W – S)
      Serviceability (S – W –S)
      Structural integrity

## Slide 34: Evaluation criteria
Facilitate the identification of differences
  Relatively “poor “ sections
  Relatively “average” sections
  Relatively “good” sections
  Relative to past traffic loading

## Slide 35
µ = mean
σ = standard deviation
X, Y = percentile values
α = percentage of data
Y
X
α1
α2
α3
α1
α2
α3
~
~
X = µ + 0.45σ
Y = µ - 0.45σ

## Slide 37: Identification of uniform sections
All information
  As built & history
  Loading
  Visual condition
  Surveillance measurements

## Slide 39: Identification of uniform sections
Surveillance measurements
  Cusum
  Normalized Cusum
  Combination of data

## Slide 40: Normalized cusum

## Slide 42: Detailed assessment
Cause and mechanism of distress
Pavement situation of each uniform pavement section

## Slide 46: End of detailed assessment
All details of each section
Know what is wrong
Know cause and mechanism of distress
Identified applicable rehab options
Proceed with design

## Slide 48: Rehabilitation options & design approach
Applicability
  Advantages/limitations/disadvantages
Design methods
  Deflection
  DCP
  Mechanistic

## Slide 49
Costs of implementation
Confidence and benefits
Level of sophistication
Level of expertise required
Not
practical
b/c ratio
too low
Non- simplified
Mech design
Design curve
Behaviour catalogue
Empirical/ theoretical
Design charts

## Slide 52: Life-cycle cost comparison
PPWOC
  Agency costs
  Road user costs
Probability theory
REACT to be incorporated

## Slide 53: 2006 TRH12
300 + pages - to be shortened
Background to recommendations to be removed – use references
Traffic loading = TRH16
Incorporate typical document contents pages in line with practice
  Eg Scoping Report, IA Report, DA Report, ect