## Slide 1: Bituminous Stabilized Materials: Structural Design and Materials Classification
RPF
November 2007
Fenella Long

## Slide 2: Today’s Presentation
Demonstrate the software for
  Pavement design method
  Materials classification method
Review process

## Slide 3: Software
www.bitstab.roadrehab.com
Software runs on website
Background info
  Descriptions
  Download backup reports

## Slide 4: Example

## Slide 5: Materials Classification
Rational and consistent method of assigning materials to a class
Example

## Slide 6: Review Process
Need industry representatives to review – YES YOU
  Structural design method
  Approach to material classification
  Material class limits
  “Reasonableness” of results

## Slide 8: Example, Moderate Region
118 MPa
6. Calculate Layer ELTS Values
118 MPa
4. Adjust for cover (118 MPa)
1. Material Classes
2. Determine subgrade stiffness (140 MPa)
3. Adjust for climate (126 MPa)
CBR 7-15%
180 mm G6
200 mm C4
150 mm BSM2
150 mm G7
5. Assign modular ratio’s and max stiffness
MR = 1.8, EMax = 180
MR = 3, EMax = 400
MR = 2, EMax = 450
7. Layer PN = thickness * ELTS
8. PN =  layer PN
6. ELTS = min (Esupport * MR , Emax)
ELTS = min(212,180)
ELTS = 180
ELTS = 400
Thickness Adj = 0.4
ELTS = 450
BCF = 0.7
Notes: Let’s look at how this would work in practice.
First of all, we start with our basic design inputs. For this method, that would consist of the layer thicknesses, the assignment material classes and the subgrade CBR.
The material classification would be obtained with the method that I just explained, so two designers starting off with the same set of basic pavement condition data should obtain exactly the same materials classification.
We next use the subgrade CBR to obtain a subgrade class, this subgrade class is used to determine the long term effective stiffness of the subgrade.
Next, we adjust this stiffness to take climate and thickness of cover into account. This implicitly models subgrade softening behaviour.
We now use our assigned material classes to determine for each pavement layer the modular ratio and the maximum allowed stiffness for the material. These parameters are fixed for each class, so the designer cannot fiddle with the stiffness to get the answer he/she wants. Also, by using the modular ratio, the stress-sensitivity of the stiffness is implicitly taken into account.
So we work from the bottom up and determine the long term effective stiffness of each layer.
Next we use a linear elastic model to determine the octahedral shear strain at several depths in each pavement layer. We add these strains to give us a relative index, called a Pavement Number, which is can be related to an expected structural capacity.
Finally we do a check on the subgrade strain to double check that the subgrade cover is sufficient.

## Slide 9: Assigning Material Class Confidence for Specific Indicators
G2
G3
G4
10th Percentile Value
90th Percentile Value
Median Value
Relative certainty that material is a G2, based on this test
e.g. DCP