## Slide 1: South African Pavement Design Method (SAPDM) Revision RPF Feedback 7th May 2008 Louw Kannemeyer

## Slide 2: Historical Overview – SAMDM
The SAMDM used since 1980s in various forms
  Any method is better than no method
  National DoT insisted that consultants design using SAMDM
    Attempt to introduce more “Science” and reduce “Art”
    ELSYM 5
  SAMDM used for developing design catalogues in 1984 and 1995
    TRH 4
  Wide-scale design software implementation since 1995
    MEPADS, Rubicon, Cerano
  Further development of engineering models slowed down because of a lack of funding since early 1990s

## Slide 3: Typical SA Pavement and SAMDM
35mm Wearing course
150 mm Crushed stone base
150 mm Cemented subbase
150 mm Granular upper selected subgrade
In situ subgrade
150 mm Granular lower selected subgrade
SA Pavement Structure
Current ME
Damage Model
Asphalt Fatigue – Freeme 1970s
Permanent Deformation FOS
Maree 1970s to 1980s
Effective Fatigue and Crushing Failure
De Beer 1980s
Vertical Strain Criteria
Dorman and Metcalf 1965
Vertical Strain Criteria
Dorman and Metcalf 1965
Vertical Strain Criteria
Dorman and Metcalf 1965
Current SAMDM has number of limitations, i.e. no damage models for plastic deformation in Asphalt layers, number of models outdated, etc, etc

## Slide 4: SAMDM - Current status
Summary
  Classical ME design method - single estimate of bearing capacity
  Critical layer approach – distress mechanisms disconnected
  Separated resilient response and damage models
  Material resilient response
    Recommended Mr and Poisson’s Ratio values
      Conflict between slow and dynamic test results
Users are disillusioned with the method
  Counter-intuitive and inadmissible results
  Extreme sensitivity of the method to input data
  Inconsistent input
    Resilient response (FWD, MDD, Laboratory)
    Strength parameters
Statements made that ME-design is not possible due to:
  Too many unexplained effects (chaos)
  Getting the right answers for the wrong reasons (i.e. SAMDM correctly predicted expected life, but predicted failure layer as being subgrade, yet it actually is base !)
SAMDM require extensive revision !!!

## Slide 5: SAPDM Revision
Overall objective
  To develop a design method that is:
    Accurate (theory must agree with reality)
    Impartial in terms of pavement type selection
      Unbound (Crushed stone, natural gravel)
      Stabilised (Cement, Foamed-bitumen, Emulsified-bitumen)
      HMA
      Concrete (not included in flexible pavement design R&D process)
Pavement Design Task Group
  Submitted R&D framework in November 2005
    Characteristics of new pavement design method
    R&D topics
      Demand analysis (Traffic and environment)
      Material resilient response models
      Pavement resilient response models
      Damage models
      Probabilistic and recursive schemes
    Each R&D topic have a number of identified R&D needs
    Each R&D need translated into one or more detailed project briefs to address the need – November 2006
Theory
Reality
=

## Slide 6: New South African Pavement Design Method (SAPDM)
Pavement Performance Information System (LTPP)
  Material Classification Concept
  Pavement Number Concept
  Validate and Calibrate ME Analysis System
Mechanistic-Empirical Analysis System
  Two components
    Engineering models
    Simulation schemes
  Based on separated response analysis
    Resilient response and damage models
  Static resilient pavement response analysis
  Damage modelling
    Pavement system as a whole contribute to permanent deformation
    Stiffness reduction for bound layers – Reflective cracking excluded
  Material resilient response and damage model calibration
    Imposed stress/strain
    Field variables – Temp, MC, Dens, etc.

## Slide 7: SAPDM Revision – Current Status
South African Pavement Design Method Process
  Pavement Performance Information System (LTPP)
    50 Projects Completed – February 2008
  Mechanistic-Empirical Analysis System (MEAS)
    Phase 1 – Develop Detailed Project Briefs – November 2006
    Phase 2 - Inception Phase (22 Projects) – July 2007
      Investigate available solutions
      Finalize project methodology
      Finalize cost and resource allocation
    Inception Report Peer Review – November 2007
    Phase 3 – Project Delivery
      Immediate Deliverables (12 to 18 months);
      Short Term Deliverables (18 months to 3 years);
      Medium Term Deliverables (3 to 5 years), and
      Long Term Deliverables > 5 years.

## Slide 8: SAPDM Revision – PPIS
PPIS developed as Internet website
  www.ppis.roadrehab.com

## Slide 9: SAPDM Revision – PPIS
Table View

## Slide 10: SAPDM Revision – PPIS
Graphical View

## Slide 11: SAPDM Revision – PPIS
Representation of 50 Captured Sections

## Slide 12: SAPDM Revision – PPIS
Typical Performance Trends
  Granular Base / Cemented Subbase

## Slide 13: SAPDM Revision – PPIS
Typical Performance Trends
  Asphalt Base

## Slide 14: SAPDM Revision – PPIS
What Next ?
  Launch PPIS website and obtain feedback from the industry;
  Perform ongoing improvement of the concept of web-based access to pavement performance information;
  Review Bitumen Stabilised Material Project Sections and include 15 sections into PPIS;
  Incorporate the Data Collection Framework into the SANRAL Manual M1;
  Standardize submittal of all design data with the Project Design Documentation based on the proforma electronic PPIS Database File.
  Development of a First Level Performance Based Design Method.

## Slide 15: SAPDM Revision – MEAS Phase 2 Outcomes

## Slide 16: SAPDM Revision – MEAS Phase 2 Outcomes
Phase
Start date
End Date
Estimated Cost
Cumulative Cost
Immediate (18 months)
Apr 2008
Dec 2009
R 41 740 599
R 41 740 599
Short-term (3 years)
Apr 2008
Mar 2011
R 6 291 064
R 48 031 623
Medium-term (5 years)
Apr 2008
Mar 2012
R 4 875 854
R 52 907 477
Long-term (10 years)
Apr 2008
Mar 2017
R 2 109 423
R 55 016 900
The Costs ?

## Slide 17: SAPDM Revision – MEAS Peer Review
Phase 2 outputs from the individual projects was synthesised into a single summary report.
All Reports subject to peer review:
  Prof Andre Molenaar (Netherlands);
  Prof Fred Hugo (Stellenbosch),
    Dr Pieter Strauss
    Dr Pieter Poolman, University of Oregon USA
    Dr Andre Smit, National Center for Asphalt Technology (NCAT), Auburn, USA
    Dr Imad L. Al-Qadi, Center for Transportation, University of Illinois, USA
    Dr Don Christensen PE, Advanced Asphalt Technologies, USA
    Dr Ramon Bonaquist PE, Advanced Asphalt Technologies, USA .

## Slide 18: SAPDM Revision – MEAS Peer Review
“having an extremely advanced pavement design engine implemented in an inadequate planning process will not address South Africa’s needs”
Must take full cognisance of the in-service operating conditions of the pavement and the impact thereof on the design inputs
Functional performance simulation must be an integral part of the pavement design process
A comprehensive cost-benefit analysis procedure assessing different life-cycle strategies and including cost and benefits for road users as well as road authorities must form part of the final deliverable
For the successful implementation and utilisation:
  Be easy to use on a day to day basis by pavement engineers
  Keep input data to essential minimum that is readily available to the user
  Relay on results of test equipment generally available in practice
  Not require knowledge that goes beyond what can reasonably be expected of an educated pavement engineer in practice

## Slide 19: SAPDM Revision – MEAS ???

## Slide 20: SAPDM Revision – MEAS
What Next ?
  Finalise the end product framework and inter dependencies;
  Adjustments to the current project plan based on:
    Inclusion of functional performance simulation (roughness, texture, friction …) – Close gap between PMS and Design;
    Inclusion economic analysis of design alternatives and maintenance strategies;
    Consideration of the project funding available.
  Project teams to re-evaluate project deliverables and how it will fit in to final product as first task during phase 3 – Get common understanding of envisaged end product.
  Revised Phase 3 to start June 2008.